## Slide 1: Modern Front-end Support in gem5
Bhargav Reddy Godala, Nayana Prasad Nagendra, Ishita Chaturvedi, Simone Campanoni, David I. August
PRINCETON
UNIVERSITY
Liberty Research Group
Arcana Research Group

## Slide 2: Introduction
We have seen that aggressive Out-of-Order CPUs tolerate data miss latency.
Modern CPUs employ decoupled front-end to tolerate instruction miss latency.
What is a decoupled front-end?

## Slide 3: State-of-Art Front-end
I-Cache
Fetch Engine
Front-end
Branch Re-steer Address
IFU
NIP
BPU
IAG
Decode
Back-end
Traditional Front-end
3
FTQ: Fetch Target Queue
IFU: Instruction Fetch Unit
BPU: Branch Prediction Unit
IAG: Instruction Address Generation
NIP: Next Instruction Pointer
EMISSARY, Nagendra and Godala, et al.
Notes: To tolerate instruction cache miss latency modern processors implement decoupled front-end. What is a decoupled frontend? I’m going to show it by modifying a traditional front-end. Here is a traditional frontend pipeline. In this design address generation unit is inside Instruction Fetch Unit. Which feeds fetch engine with a PC of next instruction to fetch from I-Cache. In a decoupled front-end address generation unit is decoupled from Instruction Fetch Unit. <click>.

## Slide 4: State-of-Art Front-end
I-Cache
Fetch Engine
NIP
BPU
IAG
Decode
Back-end
Front-end
FTQ
Prefetch
IFU
Branch Re-steer Address
Fetch Directed Instruction Prefetching Pipeline (FDIP) [Glenn Reinman et al., MICRO’99]
3
FTQ: Fetch Target Queue
IFU: Instruction Fetch Unit
BPU: Branch Prediction Unit
IAG: Instruction Address Generation
NIP: Next Instruction Pointer
EMISSARY, Nagendra and Godala, et al.
Key Idea: Prefetch in the predicted path
Notes: Now, a Fetch Target Queue is inserted in between IAG and IFU. Each entry of FTQ represents a basic block. Prefetch engine takes entries from FTQ and issues prefetch requests to Instruction Cache. Even fetch is stalling Address generation unit keeps feeding FTQ with addresses in the predicted path. If we have perfect prediction front-end would never stall. Unfortunately that is not the case. Due to this design I-Cache misses have unequal costs.

## Slide 5: Design

## Slide 6: Challenges in Implementing FDIP in gem5
Fetch stage is already complex.
Dynamic Instruction objects are constructed before BPU is invoked.
  Branch Instruction is needed to invoke BPU.
Sequence numbers are used to squash mis-speculated instructions.

## Slide 7: Branch Sequence Numbers
Unique sequence number to identify branch.
Every dynamic instruction contains:
  A sequence number
  Branch Sequence of prior branch
BrSeq Seq | Seq | Instruction
10 | 100 | Br
10 | 101 | I0
10 | 102 | I1
10 | 103 | I2
11 | 104 | Br
11 | 105 | I3
11 | 106 | I4
11 | 107 | I5
Notes: Talk about how squash works.

## Slide 8: Fetch Target Queue (FTQ)
Each entry consists of:
  A begin address (target of prior branch)
  End address (branch PC)
  Target address
  Branch Sequence number

## Slide 9: Prefetch Engine
Prefetch Buffer:
  Address to prefetch
  Issue one prefetch and insert into Fetch Buffer
F0
F1
F2
FTQ
L0
L1
L2
L3
L4
L5
L6
Prefetch Buffer
Fetch Buffer
L0
L1
L2
L3
Ready
Pending
F0
F1
F3
Prefetch request issued

## Slide 10: Modified Fetch Stage

## Slide 11: Optimizations

## Slide 12: Basic Block Based BTB
Index | Traget
br1 | target1
br2 | target2
br3 | Target3
PC based BTB
Index | Target | Branch
target1 | target2 | br2
target2 | target3 | br3
BBL based BTB

## Slide 13: Pre-decode And Early Correction
BBL BTB are indexed using beginning of a basic block.
Beginning of a basic block is identified:
  Using the next instruction following a branch instruction.
Early Correction:
  When an unconditional branch is predicted not taken.
  Flush FTQ and restart by using the pre-decoded target.

## Slide 14: Branch Predictor Changes
BBL Based Branch Predictor lookup.
Branch Sequence numbers.
ITTAGE indirect predictor support.

## Slide 15: X86 vs ARM
X86:
  Variable width instructions
  Pre-decoding is very expensive
  Micro Sequenced Ops
  Exception handling using ROM
ARM:
  Fixed width instructions
  Pre-decoding is not expensive

## Slide 16: Micro Branches in X86
In X86 there are instructions which are dynamically decoded to loops.
  Example: String copy
These branches are not inserted into BTB.
This is handled as a special case:
  These are not seen by the FDIP pipeline.
  At the time of fetch; a back edge is predicted taken.
  FTQ will not be flushed till a squash from later stages is received.

## Slide 17: Performance Bug Fixes
Perfect recovery of branch history.
TAGE Bimodal table roll back.

## Slide 18: Evaluation

## Slide 19: Performance of ARM workloads with FDIP
IPC Performance improvement of ARM workloads in % over No FDIP baseline
Field | Alderlake like
ISA | ARM 64-bit
L1I | 32KB
L1D | 64KB
L2 | 1MB (16-way)
L3 | 2MB
FTQ | 24 entry 192 inst
Width | 8-wide
ROB Size | 512 entries
IQ/LQ/SQ | 240/128/72
BPU | TAGE, ITTAGE
BTB | 16K entries
gem5 O3 CPU simulation parameters

## Slide 20: Performance of X86 workloads with FDIP
IPC Performance improvement of X86 workloads in % over No FDIP baseline
Field | Alderlake like
ISA | X86 64-bit
L1I | 32KB
L1D | 64KB
L2 | 1MB (16-way)
L3 | 2MB
FTQ | 24 entry 192 inst
Width | 8-wide
ROB Size | 512 entries
IQ/LQ/SQ | 240/128/72
BPU | TAGE, ITTAGE
BTB | 16K entries
gem5 O3 CPU simulation parameters

## Slide 21: Performance of X86 SPEC17 workloads with FDIP
IPC Performance improvement of X86 SPEC17 workloads in % over No FDIP baseline
Field | Alderlake like
ISA | X86 64-bit
L1I | 32KB
L1D | 64KB
L2 | 1MB (16-way)
L3 | 2MB
FTQ | 24 entry 192 inst
Width | 8-wide
ROB Size | 512 entries
IQ/LQ/SQ | 240/128/72
BPU | TAGE, ITTAGE
BTB | 16K entries
gem5 O3 CPU simulation parameters

## Slide 22: Published Works
EMISSARY: Enhanced Miss Awareness Replacement Policy for L2 Instruction Caching at ISCA’23
Session 2B

## Slide 23: Conclusion
We implemented FDIP in gem5.
A significant speedup over baseline.
This work was used in EMISSARY [ISCA’23].
Available at https://github.com/PrincetonUniversity/gem5_FDIP
Workloads: https://tinyurl.com/yjsc2aw4
Workloads
gem5 + FDIP

## Slide 24
Thank you
Questions?